## Slide 1: Connecticut DOT Data Management for Asset Management
William S. Pratt, P.E.
AEC Applications (Architectural, Engineering, Construction)
Karen M. Riemer, P.E.
Transportation Asset Management
Notes: Acknowledge Bill Pratt – he has been the force behind standardizing our data
AMG works closely with AEC Applications Group (Architectural, Engineering and Construction)

## Slide 2
TAMP and Data GAP Timelines
TAMP
Data
GAP
Data Planning
Identify Gaps
Establish Standards
Layout Plan to Improve
Implement Plan
TAMP Startup
Bridge & Pavement Workshops
Objectives, Risk and Financial Workshops
DRAFT TAMP
Final TAMP
Apr 2015
Nov 2015
Feb 2016
Sep 2016
Dec 2016
Notes: Before we get started  a little background.
Two timelines (TAMP and Data Gap)
Early on realized importance of asset data systems for our TAMP
Data Sharing identified in Gap Analysis

## Slide 3: Highway TAMP Assets
Pavements
Bridges
Sign Supports
Signals
Signs
Pavement Markings
Retaining Walls
Guiderail
Curb Ramps
Lighting & Illumination
Fleet
Buildings
ITS
…
Initial TAMP
Future TAMPs
Notes: Pavement and Bridge as Required
Plan to include others depends on rulemaking  Internal
List of Assets goes on and on … Rumble strips, Outflows and drainage systems, commuter lots

## Slide 4: Goals
Keep Asset Inventories Updated
Maximize Data Integration
Notes: Keep the authoritative database for asset inventory updated with accurate and timely data.
Maximize data integration to remove duplicate data collection and reduce confusion as to which is most recent data.

## Slide 5
Current Asset Inventory Systems
TED
PCD
Transportation Enterprise
Data
Project Composite Data
Notes: Basic layout of our inventory systems
Last 2 years  moved to production on two systems in the cloud
Databases and spreadsheets
   moving towards putting inventories on one of the two platforms (Facilities to Inspecttech / Signs and Guiderail to EXOR will be discussed more in detail)
   depends if reoccuring assessments and extent of inventory information collected.

## Slide 6: Where do the assets get changed during their life?
Construction
Maintenance
Permits
Notes: - Important step to identify where our assets get touched throughout their life cycle.
- Then broke each down as to how we can capture this work data best.

## Slide 7: Identifying Assets in Capital Construction Projects
Update Identification
of Assets @
Final Design Plans
Update Asset Inventory and Conditions @ Construction Complete
Project
Timeline
Asset s
Timeline
Preliminary Identification of Assets @
Project Request
Notes: Let’s start with Capital Projects.
First these projects can take anywhere from 3 to 10 years to get to construction.
This period of time was taking too long to wait to know what was happening to an asset.
Identified 3 points along the life of a project to capture asset data  Project Request  Final Design  Construction Completion
We are starting with doing this for just a few assets whose authoritative inventory databases are tied to our Project Document Management System ???????.

## Slide 8: Identifying Assets in Capital Construction Projects
Notes: Here you can see for a particular project: Bridges, Sign Supports and Signals are identified in the Project Composite Database.
This information is entered at Project Request and updated at Final Design.

## Slide 9: Identifying Assets in Capital Construction Projects
Notes: Projects are no longer shown as a point on a map but rather as a polygon.
The polygon is stored in the TED (Transportation Enterprise Database). The TED also contains asset data directly from the asset inventories which it links with the project data which resides in a system we call PCD (Project Composite Database). This is where the assets included in a project is listed.
Projects are displayed by color corresponding to the phase that the project is now in. This coloring is based on dates from a variety of resources: finance’s obligation plan, engineering’s project composite database, and construction’s payout system. Although some of the date entries are manual for local projects we are working on a process to remove the manual effort.
This project mapping has been a very critical tool in that prior to this mapping, designers, maintainers and permit developers did not have a single source to know what work was happening around them or in some cases through them. We have experienced some situations where multiple parties were on a work site at the same time through three different avenues.

## Slide 10: Harvesting Assets in Capital Construction Projects
CAD Design
CAD Assets to GIS
Asset DB Proposed
Field Verify
Asset DB Confirm

## Slide 11
SF of Sign Face
SF of Sign Face
+
Structure
+
Foundation
Harvesting Assets in Capital Construction Projects
Extruded Aluminum

## Slide 12: Harvesting Assets in Capital Construction Projects

## Slide 13: Identified Who Will Collect and When
SIGNS | GUIDERAIL

## Slide 14: Identified What Will Be Collected
Guiderail
  Guiderail Segment
  Location
  Type
  End Terminals
  Installation/Removal/Repair Date
  Installer
  Images / Photos
Signs
  Sign Id
  Location
  Mounting Type
  Sheeting Type
  Installation/Removal Date
  Manufacturer
  Manufacture Date
  Images / Photos
  White  Verify CAD Attributes
  Orange  Field Capture Input

## Slide 15: Challenges CTDOT Faces:
  Implementing Business Processes (Users, Technology, QA/QC)
    Harvesting Assets at Design
    Field Capture of Asset Data at Work Completion
  Incorporate Pavement Asset Data
  Integrate all Asset, Road Network and Project Management Systems wherever possible to avoid duplication of efforts and out-of-date data.

## Slide 16: Progress CTDOT Made:
  Developed a Common Linear Reference System (LRS)
  Identified Authoritative Asset Databases
  Tracking Assets within Projects