## Slide 1: Guide to Data and Information Sharing Workflows Across the Life Cycle of Transportation Assets
June, 2016

## Slide 2: Outline
Information delivery manual (IDM)
An example of IDM
Plan to develop IDM for transportation assets

## Slide 3
Data sharing guidance in the vertical sector
Information Delivery Manual (IDM)

## Slide 4: Business use case
A scenario within the life cycle of project in which data exchange is required to enable the completion of a product of the project.
Examples:
  The data exchange between architects, structural engineers and HVAC engineers to develop an as-designed model
  The data exchange between engineers and cost estimators to support quantity take-off and cost estimation
  The sharing of the design models to the energy analysis process
3 elements of a use case
  Tasks to be completed
  Actors/stakeholders
  Data exchange requirements

## Slide 5: IDM
Process map
Exchange requirement (ER)
IDM aims to answer
  processes in which data sharing is required
  data producers and receivers
  specific data attributes required for a data sharing scenario

## Slide 6: IDM
Aim to capture the industry knowledge and experience about the workflow and information sharing flow of a business use case.
Goals:
  Identify and describe the processes in which data sharing is required
  Identify the data requester and receiver for each data sharing scenario
  Document the specific data requirements for a data sharing scenario
2 core components
  A process map which explains the sequence of activities to be completed and the actors (stakeholders) involved
  Exchange requirements (ER) which specify what data entities/attributes to be transferred to whom and by whom

## Slide 7: Process Map
A process map describes:
Tasks (activities) to be performed.
Sequencing of tasks.
Actors (people/organizations) involved.

## Slide 8: Exchange Requirement (ER)
ER defines what data/information to be shared.
Audience is the user (architect, engineer, constructor, etc.)

## Slide 9: IDM-ER in Process Map
This is an integrated map of process and exchange requirements,
This map shows what data to be shared to whom and when.

## Slide 10: Overview of IDM Projects
04 Approved
01 Under review
12 Draft
18 Work in progress
06 Proposal

## Slide 11
IDM for precast concrete

## Slide 12: Scope
This IDM focuses on the data exchanges between architects, engineers, general contractors and precast fabricators from the beginning of the programming phase to the end of the fabrication phase.

## Slide 13: Process map
actors
phase
tasks
exchange requirement

## Slide 14: Written descriptions of Process map
Task description
ER description

## Slide 15: Detailed specification of ER
ERs
Data Attributes

## Slide 16
IDM for transportation assets
DEVELOPMENT PLAN

## Slide 17: Assets to be investigated
Sign
Culvert
Guard rail
Pavement
Bridge
Others?

## Slide 18: Business use case to be investigated
Owner and architects?
Architects and engineers?
Architects and engineers and contractors?
Contractors and asset managers?
Engineers and cost estimator?
Other?
The top prioritized use cases will be developed first!

## Slide 19: Workgroup members
Research team
Industry professionals
  Selected based the business use case
  Potential experts: architects, designers, contracts, asset managers, software vendors

## Slide 20: IDM development cycle
Meeting 1
IDM development
Meeting 2
Workgroup discussion
Output: data exchange narratives
By ISU team
ISU team and research panel
Output: detailed IDM
Individual discussions with workgroup members (if necessary)
Present findings
Output: approved IDM

## Slide 21: Meeting 1
Workgroup members will discuss:
  Workflow which specifies what tasks to be completed and actors involved
  Locations in the workflow where data sharing occur
Output: high level workflow and data sharing narratives

## Slide 22: IDM development
Input: narratives from meeting 1
ISU team examines the input and develop a detailed and formal process map and ER matrix
Further inputs can be retrieved from individual meetings between ISU team and the workgroup members
Output: a detailed IDM

## Slide 23: Meeting 2
The findings will be presented to the research panel
Output: an approved IDM

## Slide 24: Discussions
Implementation plan?
Mapping between identified exchange concepts and data entities attributes in software applications?